## Slide 1
DEEP LEARNING THEORY–BASED PRACTICAL WORK
Phase 2 · Solution Design
Cross-Subject Motor Imagery EEG
Classification using Deep Learning
A hybrid convolutional–Transformer approach evaluated on unseen subjects
Team members
[ Names and registration numbers ]
Guide / faculty
[ Name and designation ]
Course
[ Course code and title ]
Date
15 September 2026
Notes: Phase 2 presents the solution design: how the literature survey from Phase 1 becomes a concrete, implementable project plan. Fill in team, guide and course before presenting.

## Slide 2
PROBLEM STATEMENT
Decoding imagined movement from scalp EEG
2
When a person imagines moving a limb, the sensorimotor cortex shows a measurable drop in mu-band power on the opposite side of the head. The task is to recover which movement was imagined from that signal.
Low signal-to-noise ratio
Cortical activity is attenuated by the skull and scalp, and is mixed with eye, muscle and mains interference
Small, high-dimensional data
A four-second trial holds over twenty thousand samples, but each subject provides only a few hundred labelled trials
Variability between people
Skull shape, electrode placement and mental strategy differ, so feature distributions shift from subject to subject
Notes: Three difficulties: noise, data scarcity, and subject variability. The third is the one this project targets.

## Slide 3
LITERATURE SURVEY SUMMARY
From compact CNNs to convolutional–Transformer hybrids
3
What improved
Each step added a better way to relate information across the whole trial, rather than only within a short window.
What it cost
Parameter counts rose from roughly two thousand to over one hundred thousand, and the data requirement rose with them.
Notes: The four papers form a progression: CNN, then CNN with attention and temporal convolution, then CNN with a Transformer encoder. Capability rose, and so did cost.

## Slide 4
RESEARCH GAP
Four limitations common to the surveyed work
4
1
Cross-subject generalisation remains difficult; accuracy falls when the test subject is unseen.
2
Zero-calibration and low-calibration operation is still an open problem.
3
CNNs are lightweight but limited in modelling long-range temporal structure.
4
Transformers capture global relationships but cost more and need more data.
The clearest illustration
CTNet is the strongest of the four within subject, yet loses 23.88 points on the four-class task when the test subject is unseen.
What is needed
A model that balances classification accuracy, model complexity and generalisation to new people, rather than optimising any one of them alone.
Notes: CTNet is the clearest illustration: 82.52 per cent within subject, 58.64 per cent on an unseen subject. Nearly twenty-four points.

## Slide 5
PROJECT OBJECTIVES
What the project sets out to do
5
1
Implement a reproducible preprocessing and evaluation pipeline for BCI Competition IV Dataset 2a.
2
Implement EEGNet, ATCNet, CTNet and EEG Conformer as baselines under one identical protocol.
3
Design a hybrid model combining the convolutional front end of EEGNet with the attention mechanisms of the other three.
4
Train and evaluate every model using leave-one-subject-out cross-validation.
5
Measure accuracy, Cohen's kappa, precision, recall and F1-score, per subject and averaged.
6
Compare parameter count and computational cost alongside accuracy.
The final objective is to report whether the proposed combination improves cross-subject performance while remaining lightweight — and to report it either way.
Notes: Six objectives. The seventh, on the purple band, is the honesty commitment: a negative result is still reported.

## Slide 6
DATASET
BCI Competition IV Dataset 2a
6
Property | Value
Subjects | 9
EEG channels | 22
Classes | 4 — left hand, right hand, feet, tongue
Sampling rate | 250 Hz
Sessions per subject | 2, on different days
Trials per subject | 576
Total labelled trials | 5,184
Analysis window | 0.5 to 4.0 s after cue (875 samples)
Chosen because all four surveyed papers evaluate on it, so our baseline implementations can be checked against published values.
The four motor imagery classes
Each class activates a different region of the sensorimotor cortex. Hand imagery appears on the opposite side of the head, foot imagery near the midline.
With only nine subjects, leave-one-subject-out gives nine folds — enough for a mean, a standard deviation and a paired test, but not enough to treat any single fold as reliable on its own.
Notes: Nine subjects, four classes, 576 trials each. Small by deep learning standards, which is why regularisation and augmentation are necessary rather than optional.

## Slide 7
PROPOSED SYSTEM ARCHITECTURE
From raw EEG to a predicted movement
7
CNN feature extraction
Depthwise and separable convolution, adapted from EEGNet. Learns spatial filters at very low parameter cost.
Temporal attention
Windowed self-attention, adapted from ATCNet, CTNet and EEG Conformer. Relates distant parts of the trial.
Notes: The two shaded stages are the learned components. Everything else is fixed signal processing or output layers.

## Slide 8
PROPOSED METHODOLOGY
Step-by-step pipeline
8
Stage | What happens | Why it matters
Preprocessing | Band-pass 4–38 Hz, epoch 0.5–4.0 s, alignment, normalisation | Identical for every model, so differences come from the models
Feature extraction | Convolutional block followed by windowed attention | The learned part of the system
Model training | Subject-independent, validation on a held-out subject | Avoids selecting hyperparameters that favour within-subject fit
LOSO evaluation | Nine folds, each with a different unseen test subject | Measures what a new user would experience
Performance analysis | Metrics per subject, plus a paired statistical test | Averages alone hide failures on individual subjects
Notes: Seven stages. Highlighted ones are where the technical work sits.

## Slide 9
BASELINE COMPARISON
Four published baselines and the proposed model
9
Model | Architecture type | Main strength | Main limitation | Role in our experiments
EEGNet (2018) | Compact CNN | Very small; trains reliably on limited data | Limited long-range temporal modelling | Lower bound on model size
ATCNet (2023) | CNN + attention + TCN | Attention applied locally, suits short trials | Considerably larger than EEGNet | Source of the windowed attention idea
EEG Conformer (2023) | CNN + Transformer | Global self-attention with interpretability | Costly; needs augmentation to train well | Reference for convolution-then-attention
CTNet (2024) | CNN + Transformer | Highest reported within-subject accuracy | Large drop under subject-independent testing | States the research gap quantitatively
Proposed HCT-Net | CNN + windowed attention | Combines the components above at 20,996 parameters | Not yet evaluated | The model under investigation
Published accuracies are not shown side by side here because each paper used a different evaluation protocol, so the figures cannot be ranked against one another. Re-running all four under one leave-one-subject-out protocol is part of this project.
Notes: Important point to make aloud: the published numbers use different protocols. EEGNet is quoted at 68.67 per cent by one paper and 71.50 by another, for the same model on the same dataset.

## Slide 10
EVALUATION STRATEGY
Leave-one-subject-out evaluation
10
Accuracy
Mean and standard deviation over nine folds
Cohen's kappa
Corrected for chance agreement
Precision, recall, F1
Macro-averaged over the four classes
Parameters and time
Model complexity and computational cost
A Wilcoxon signed-rank test, paired across the nine subjects, is used to decide whether a difference between two models is meaningful. Results are reported per subject as well as averaged.
Notes: Nine folds. Seven training subjects, one validation subject, one test subject. The validation subject is held out too, which matters for honest hyperparameter selection.

## Slide 11
EXPECTED OUTCOMES AND NOVELTY
What we expect, and what is actually new
11
Expected outcomes
Better generalisation to unseen subjects than the heavier baselines
Competitive motor imagery classification accuracy
A lightweight architecture — 20,996 parameters, about one fifth the size of ATCNet
Reduced dependence on subject-specific calibration
What the project contributes
A comparison of all four architectures under one identical LOSO protocol
A specific lightweight combination, with attention depth reduced to suit the dataset size
A component-wise study showing what each part contributes to cross-subject accuracy
Accuracy measured against parameter count under a single protocol
These are expected outcomes, not results.
No experiments have been run at this stage. The individual components are all taken from published work; what is proposed is the particular combination, the subject-independent evaluation, and the study of what each component contributes.
Notes: Say this explicitly: nothing on the left has been measured. The novelty claim is modest and deliberate — a careful comparative study plus a concrete lightweight design.

## Slide 12
PHASE 3, 16 SEPTEMBER TO 3 OCTOBER
Implementation plan and conclusion
12
In summary
The literature survey identified a specific, measurable gap: cross-subject accuracy falls sharply, and closing it currently costs model size. Phase 2 turns that into an implementable plan — one dataset, five models, one evaluation protocol, and a fixed schedule. The plan is deliberately front-loaded, so that the pipeline and baselines are verified before the proposed model is written.
Notes: Close here. The point of Phase 2 is that the survey has become a concrete plan that fits the remaining time.